## Slide 1: Disposal of waste containing mercury
Sven Hagemann GRS

## Slide 2: Whate are Mercury Containing Wastes?
Other mercury compounds
End of life products
Stabilized mercury

## Slide 3: Management Options for Mercury Containing Wastes
Other mercury compounds
End of life products
Permanent storage in underground mines
Specially engineered landfill
Temporary storage
Use
Extraction
Stabilization
?
Stabilized mercury
Temporary storage
Temporary storage
?

## Slide 4: Other, not recommended disposal options
Batteries
End of life products
Permanent storage in underground mines
Specially engineered landfill
Direct disposal without treatment
Stabilized mercury
Municipal waste landfill
Direct disposal  hydrogen gas generation (corrosion)
 Source of mercury emissions during disposal and after closure

## Slide 5: Important steps in managing Mercury containing wastes
Separate Collection
  Waste Collection Stations or Drop-off Depots
  Collection at Public Places or Shops
  Collection at Households by Collectors
Storage pending recycling/ extraction operations

## Slide 6: Important steps in managing Mercury containing wastes
Recycling/ extraction operations
  Pre-treatment
  Thermal treatment
Management of extracted mercury
  Storage
  Stabilization
Final disposal (operations not leading to re-use)

## Slide 7: Treatment and disposal of mercury containing lamps
Mechanical crushing + sieving
Glas (containing Hg)
Metal end caps (containg Hg)
Sealed with constant exhaust gas control
Phospor powder (containing Hg)
Thermal treatment Rotary kiln/ vaccum mixer
Glas (Hg-free)
Metal end caps (Hg free)
Phospor powder (Hg free)
Re-Use
Re-Use
Re-Use
Condensation

## Slide 8: Treatment and disposal of mercury containing batteries
Separation
Mercury containng batteries
Sealed with constant exhaust gas control
Mercury free batteries
Thermal treatment
Metal Scrap
Re-Use
Mixed batteries
Metall recycling
Condensation

## Slide 9: Recycling and disposal – some general observations
Separate collection
With few global exceptions, collection quota for mercury added products are low or negligable  Larger part:  municipal waste  solid waste landfill/ waste incineration
Recycling of mercury products
Performed by specialized companies, often operating internationally
As far as known, in most Asian countries no or not sufficient recycling plants  mercury waste cannot be recycled and not environmentally sound disposed

## Slide 10: Disposal of mercury containing waste – Opportunities and Challenges
Opportunities
Well established technologies exist
Recycling generates Hg-free material that may be used again
Small amount of remaining waste that has to be disposed
Challenges
Final disposal without treatment not recommended
Separate management requires effective separate collection
Recycling plants in Asia often lacking