## Slide 1
Introduction to ASGM
Lecture 1
Introduction to ASGM

## Slide 2: Introduction to ASGM

## Slide 3: Overview
What is ASGM?
Geology and Gold
Mineral Extraction
Mineral Processing
Mercury Use in ASGM
Gold Supply Chains
Formality and Governance
Spatial Distribution & Seasonality
Health and Environment

## Slide 4
ASGM (Artisanal and Small Scale Gold Mining):
Gold mining done by individual miners, communities, or small enterprises with limited capital investment and production. ASGM uses largely manual and semi-mechanised techniques.
What is ASGM?

## Slide 5
Minerals
Rocks
Gold
Where does gold come from?

## Slide 6
Where does gold come from?
gold vein
disseminated gold
gold in surface sediments
Rock containing gold that is targeted by miners = gold ore.
To produce gold, the ore must be processed to remove the other minerals.

## Slide 7
  Range from <1 to >100 g/T
  Can vary significantly between sites, and even within deposits
The amount of gold in the ore (expressed in g/T)
Ore Grade
lower grade
higher grade

## Slide 8
  The “gold” recovered from ore is typically a mix of metals
  Purity is the proportion of this mix that is gold
  Expressed in % purity (0 to 100%) or in karats (0 to 24K)
  Can vary significantly between sites and less so within a site
Gold Purity
Recovered
“Gold”
Gold
Copper
Silver
80%
10%
10%

## Slide 9
Correcting from impure to pure (24K) gold:
Weight of gold x (purity of gold/24K)
e.g., You have 100 g of 18K gold. How many g of pure gold?
100 g x 18K/24K = 75 g
100 g of 18K gold is 75 g of 24K gold
Gold Purity

## Slide 10
Hard Rock Deposits
(Primary Deposits)
Soft Rock Deposits
(Alluvial Deposits)
Mineral Deposits

## Slide 11
Open Pit
Mine Shaft
Extraction – Hard Rock

## Slide 12
Extraction – Hard Rock

## Slide 13
Extraction – Soft Rock

## Slide 14
Extraction – Soft Rock

## Slide 15: Processing
Crush
Mill
Concentrate
Burn Amalgam
Amalgamate with Mercury
Smelt/
Refine

## Slide 16: Crushing
Manual Hammering
Jaw Crusher
Hammer Crusher
Reduces size of ore rocks
Processing

## Slide 17: Milling
Ball Mill
Disk Mill
Wet Pan Mill
Reduces grain size further. Liberates gold from other minerals in the ore.
Processing
Good Liberation: grain size of the ore is fine enough to
separate gold particles from other
minerals.
* Proper grain size varies with ore.

## Slide 18
Grain size
Control
Processing
Improves recovery by ensuring the proper grain size for the best liberation of gold has been achieved.

## Slide 19: Gravimetric Concentration
Pan
Sluice
Shaking Table
Removes non-gold minerals from the milled material, reducing the total volume of the milled ore and concentrating the gold particles within it.
Processing

## Slide 20: Smelting and Refining
Processing
Melts concentrated ore or gold into a solid gold piece. The gold can be further refined (usually by a gold shop or refinery) to pure 24K gold.

## Slide 21: Where is mercury used in ASGM?
- Mercury is added to ore to extract gold
- Mercury binds easily with gold, making a heavy mercury-gold amalgam that is easier to separate from the rest of the ore
Hg
in processing
“AMALGAMATION”

## Slide 22
Mercury is added to ore to extract gold

## Slide 23: Mercury Amalgamation
Mix mercury with ore
Recover amalgam (squeeze)
Vaporize mercury
Sponge gold

## Slide 24: Whole Ore Amalgamation

## Slide 25: Concentrate Amalgamation

## Slide 26: Mercury Use
“Mercury use” in ASGM in a Minamata context means:
The net loss of mercury during ore processing
or in other words, the amount of mercury that is lost to the environment during ore processing operations.
Where is mercury lost to the environment?

## Slide 27
Mix Mercury With ore
Recover Amalgam
Vaporize Mercury
Sponge Gold
Mercury Use (loss to environment)
Hg
Hg
Hg

## Slide 28
Crush
Mill
Concentrate
Burn Amalgam
Whole Ore Amalgamation
Concentrate amalgamation
OR
Smelt/
Refine
Mercury Use (loss to environment)

## Slide 29
Crush
Mill
Concentrate
Concentrate amalgamation
Whole Ore Amalgamation
OR
Mercury Use (loss to environment)
Burn Amalgam
Smelt/
Refine

## Slide 30
Crush
Mill
Concentrate
Burn Amalgam
Concentrate amalgamation
Whole Ore Amalgamation
OR
Smelt/
Refine
Rivers, lakes, ground water
Tailings
Atmosphere
Mercury Use (loss to environment)

## Slide 31: If waste rock contains enough gold, it is sometimes reprocessed by leeching with cyanide. (worst practice banned by Minamata)
Processing
Tailings (waste)
Processing
Hg
Hg

## Slide 32: A typical workflow

## Slide 33
A typical workflow

## Slide 34
A typical workflow

## Slide 35
A typical workflow

## Slide 36
A typical workflow

## Slide 37
A typical workflow

## Slide 38
A typical workflow

## Slide 39
A typical workflow

## Slide 40
A typical workflow

## Slide 41
mine
amalgam
A typical workflow

## Slide 42
mine
amalgam
Rivers, lakes, ground water
Tailings piles
Atmosphere
A typical workflow

## Slide 43
Individuals
Small Businesses
Cooperatives
Organization of ASGM
Organization of miners

## Slide 44
Workforce
Primary ASGM workforce - number of workers directly employed in the gold production system (receive direct payment from the gold proceeds).
- miners (extraction workers, processing workers, mining/processing foremen), business owners, mining coordinators, cooperative leaders
Secondary ASGM workforce - number of people indirectly financially dependent on the ASGM sector (provide goods and services to the sector).
- agricultural producers, merchants, traders, service providers

## Slide 45
Organization of ASGM
Distribution
of Revenue

## Slide 46
Few ASGM operations adhere to national legal frameworks
Often local governance (Community, Municipality, Local police)
Understanding the governance structure can provide useful information for inventory work:
  Understand key stakeholders
  Determine who to interview
  Provide insight into local operations
Formality / Governance
Organization of ASGM

## Slide 47: Gold Supply Chain
Domestic ASM
Domestic LSM
On Site Buyer
Region Buyer
Exporter
Intern. Trader
Refiner
Refiner
Mine
Smelter
LBMA
70%
80%
90%
95%
98%
99%
LBMA
10g
100g
10kg
50kg
100kg
1000kg
10
Miners
30
Miners
5
Miners
International
International

## Slide 48
Spatial Distribution

## Slide 49: Seasonality
ASGM activity can vary greatly throughout the year, especially in regions with a heavy rainy season and seasonal flooding. During these times of the year, productivity and workforce, and thus mercury use in processing may be drastically reduced.
Relevance: Annual mercury use and gold production are often calculated by interviewing about daily productivity. It is important for a researcher to ask clear questions about the seasonality of ASGM in the region so that productivity is not over or underestimated. For example, on Site A, a baseline team finds that 1 kg of Hg is used per day on the site. Miner interviews indicate they work 5 days per week and have 10 holidays per year (250 days of work per year). This would lead the officer to believe: 1 kg Hg/d x 250 d/y = 250 kg Hg/y.
However, further questioning reveals that all extraction work stops for three months (~60 working days) of the year due to flooding. There are 190 active mining days and the annual mercury use estimate for the site is 1 kg Hg/d x 190 d/y = 190 kg Hg/y.

## Slide 50: Environmental Impact
Tailings (waste) release
To water:
increased turbidity
increased erosion
circulation changes
coastline alteration
loss of habitat
To land:
Loss of habitat
Loss of mining
opportunity

## Slide 51: Health Impact
Mercury is a neurotoxin – detrimental effects on the nervous system
  Skin contact / absorption
  inhalation

## Slide 52: Health
Hg
Hg
Hg
  ingestion

## Slide 53: Summary
3 key components of ASGM – each offering important
information that can be used for ASGM inventory
  Extraction
  Processing
  Markets
  Must understand each facet of ASGM - each is a source of valuable information
Significant variation in practices between sites, regions
and countries -- approaches will be different in every
country and will be tailored to each region within.
To understand ASGM must embrace its variability

## Slide 54: Thank you very much! Questions?