## Slide 1: Elimination of Children’s Exposure to Lead Paint: A Model Law for Regulating Lead Paint
UN Environment Workshop
Kingston, Jamaica
1 December 2017

## Slide 2: Overview of Presentation
1) Development of the Model Law
  Purpose of the Model Law
  Lead Paint Alliance-driven process
  Stakeholder involvement and opportunities for public input
2) Key Provisions
  Legal Limit on Total Lead Content
  Third-Party Testing and Declaration of Conformity
  Enforcement Tools
3) Key Considerations for Adaptation of the Model Law

## Slide 3: Part 1: Development of the Model Law and Guidance for Regulating Lead Paint

## Slide 4: Background: Does lead need to be in paint?
Historically, lead compounds were intentionally added to oil-based decorative and industrial paint to give it certain properties:
  Enhanced color, reduced corrosion on metal surfaces or faster drying time
Lead is most commonly found in oil-based paints, while water-based latex paints rarely contain intentionally added lead.
Today, non-leaded pigments, anti-corrosive ingredients and driers are widely available and are used by manufacturers to produce high quality paints
Paints may also include ingredients, such as natural clays, that contain lead as a contaminant. This is why “lead-free” paint is not technically possible, and also why testing is crucial (see upcoming slides).
Notes: Talking Points:
Before discussing why lead in paint should be regulated, it is helpful to understand why lead is used in paint and that there are alternatives to lead.
Background (Excerpted from Guidance):
Paint is typically a mixture of resins, pigments, fillers, solvents, and other additives.
Historically, lead compounds have been intentionally added to oil-based paint to give it certain properties, such as enhanced color, reduced corrosion on metal surfaces, or faster drying time. For the same reasons, lead compounds may be present in other types of coatings, including varnishes, lacquers, enamels, glazes and primers.
However non-leaded pigments, driers and anti-corrosive ingredients are widely available for use in oil-based paints, and are used by manufacturers to produce high-quality paints in all regions of the world. Increasingly, paint producers around the world are publicly stating that it is feasible to eliminate the use of intentionally added lead compounds in all paints.
Lead additives are most commonly used in oil-based paint due to their specific chemical properties, and such solvent-based lead paints and coatings are still widely available and used in many countries. Water-based latex paints rarely contain intentionally added lead compounds.
Paints may also include ingredients that contain lead as a contaminant. For example, paints may include natural clays and other raw materials that may contain residual lead content. This is why it is not technically feasible to set a “zero” limit for lead content in paint. However, when a paint manufacturer does not intentionally add lead compounds to its paints and takes into account the residual lead content in raw materials, the lead content of the paints will be low.

## Slide 5: Purpose of the Model Law
Represents global best practices in regulating lead paint, and serves as a template for a strong lead paint law
Intended to be straightforward for both governments and regulated entities to implement, and for governments to enforce
Not intended to be a one-size fits all approach, but to be adapted to each country’s unique legal framework.
Lead paint “laws” can take various forms in a country, including statutes, regulations, and enforceable standards
Notes: This slide is intended to explain to the audience why we are talking to them about a model lead paint law, and to orient them to the rest of the presentation. Key points to highlight include:
Customizable to individual country needs/framework: The Model Law is not intended to be prescriptive, and the drafters recognized that countries may make necessary changes to adjust to their circumstances. What will be emphasized during the presentation are the key elements of the Model Law, and why including them can lead to a more protective framework for regulating lead paint.
Different terminology: Though the Model Law is framed as a “law,” it may be helpful at the outset to note that depending on how different countries regulate hazardous substances, this type of measure may take the form of a law or statute, or a regulation, or even a standard. For example, Cambodia has both a code provision and a related sub-decree with its lead paint law, and Kenya’s law takes the form of a standard.

## Slide 6: Model Law Developed by the Lead Paint Alliance
Voluntary international initiative led by the United Nations Environment Program and the World Health Organization
The Lead Paint Alliance was created by a unanimous resolution at a meeting of the Strategic Approach to International Chemicals Management (SAICM) in 2009
Governments requested a model law to help establish lead paint laws
The Alliance developed the Model Law through an inclusive and transparent process
Notes: Background:
The purpose of this slide is to highlight that the Model Law and Guidance were developed through a process led by international environmental and health organizations, and that the Lead Paint Alliance was created through a consensus among the international community gathered at SAICM.
Over 175 governments participate in SAICM (see this link for a list of SAICM “focal points,” i.e., self-identified key contacts in participating countries: http://www.saicm.org/Implementation/FocalPoints/tabid/5461/language/en-US/Default.aspx)
SAICM’s overall objective is “the achievement of the sound management of chemicals throughout their life cycle so that by the year 2020, chemicals are produced and used in ways that minimize significant adverse impacts on the environment and human health.” Relatedly, the goal of the Lead Paint Alliance is to phase out the use of lead in paint by 2020.
As part of their work implementing the goal of the Lead Paint Alliance, UNEP and WHO worked directly with governments to implement effective lead paint laws. Initially, this was accomplished through a toolkit that laid out the key elements of a strong lead paint law, but lacked actual legal text. Several governments requested legal text that they could refer to in drafting their own lead paint laws. This was the impetus for the lead paint Model Law and Guidance.

## Slide 7: Process for Drafting Model Law and Guidance
Model law is based on existing lead paint laws, and includes changes to reflect lessons learned and to make it both easy to implement and customizable to national circumstances
Worked with stakeholders (industry, civil society, technical experts) on the draft, and incorporated their comments
  Global and regional paint industry associations and companies generally supportive of lead paint laws
Draft provided on the United Nations Environment web site to solicit broad public comment
Year-long process, finalized in Fall 2017
Notes: Background:
The drafting group for the Model Law and Guidance consisted of representatives from UNEP, WHO, and the U.S. Environmental Protection Agency.
To begin writing a model lead paint law, the drafting group first looked to lead paint laws from around the world, including the Philippines, the United States, South Africa, Canada, Uruguay, and others. The purpose of reviewing these laws was to gather “best practices” that could be included in a “model” lead paint law.
One example of a “lesson learned” from an existing law, is the model law strengthened and streamlined the testing requirements from the U.S. lead paint and consumer products law to make the requirements easier to understand and implement.
The Model Law takes a different approach than the approach used in the European Union REACH chemical law. The following excerpt from the Guidance explains this:
  “Countries that have enacted laws to limit the lead content in paint have generally used one of two approaches: (1) establish a set of chemical-specific regulatory limits based on the risks of individual lead compounds that are used as additives in paint (currently used in the European Union REACH regulation ), or (2) establish a single regulatory limit on the total concentration of lead in paint from all sources (currently used in 34 countries). Both approaches have been successful in limiting the lead content in paint, but the chemical-specific approach requires risk assessments of individual lead compounds that may be beyond the capacity of many developing countries. In contrast, a single regulatory limit on total lead content does not require extensive risk assessments, and is much simpler for governments to implement and enforce. Manufacturers can achieve a low legal limit on total lead content in paint by developing formulations that do not intentionally use any lead additives and that take into account potential residual lead content in raw material ingredients.”
Early in the drafting process, the drafting group reached out to key stakeholders, including governments and paint industry representatives, to get initial feedback. This outreach included the International Paint and Printing Ink Council (IPPIC), a member of the Alliance Advisory Council. IPPIC is an organization that represents paint industry groups from around the world, and has been supportive of the work of the Lead Paint Alliance. From IPPIC’s website:
  “Members of the IPPIC include the American Coatings Association (ACA), Australian Paint Manufacturers’ Federation (APMF), the Brazilian Paint Manufacturers Association (ABRAFATI), The British Coatings Federation (BCF), the Canadian Paint and Coatings Association (CPCA), the European Council of the Paint, Printing Ink and Artists‘ Colours Industry (CEPE), the China National Coatings Industry Association (CNCIA), the French Paints, Printing Inks, Artist Colours and Adhesives Association(FIPEC), the German Paint Industry Association (VdL), the Japan Paint Manufacturers Association (JPMA), the Mexican Paint and Printing Ink Manufacturers’ Association (ANAFAPYT), the New Zealand Paint Manufacturers Association (NZPMA), the South African Paint Manufacturers Association (SAPMA), and the Association of the Paint Industry in Turkey (BOSAD).”
UNEP posted the draft to its website for four weeks for public comment.
Public comments from governments, academics, NGOs, and the paint industry were received and reviewed, and appropriate changes were then made to model law. Comments from the paint industry represented both large and small to medium paint companies.
Stakeholder and public input was critical in ensuring the model law was protective and workable.
UNEP finalized the model law in Fall 2017.

## Slide 8: Summary of Model Law and Guidance
Structure: 1. Guidance; 2. Model Law
Guidance provides:
  Detailed background on the public health and economic costs of lead in paint;
  Explains the “case for legal limits” – economic and health benefits, trade benefits, setting a low concentration standard; only way to ensure low lead paint levels; and
  Presents the objectives and key elements of an effective lead paint law, such as:
  Model Law provides template language for a lead paint law
    Definitions
    Clear limit on total lead
    Setting effective dates
Compliance and enforcement provisions
Consequences for non-compliance
Notes: Background:
This slide describes the structure and content of the Model Law and Guidance, which will be walked through on the upcoming slides.
The next slide briefly presents the “case for legal limits,” which is discussed in great detail in the Guidance itself.
Note that while the Model Law and Guidance discuss “definitions,” this section is not walked through in this presentation, given that it is straightforward and fairly self-explanatory. It is worth mentioning here, so the audience is aware this section is included.
As noted in slide 5, the Model law section provides a template for language that could be used in a lead paint law. It may be worth reiterating here the earlier points about the Model Law being customizable to national circumstances.

## Slide 9: The Case for Legal Limits
Human health effects of lead exposure:
  There is no safe exposure level for children, yet there are numerous exposure pathways (peeling and chipping of paint around homes and schools, contaminated dust that is easily accessible and ingested by young children).
  Lead can cause serious health impacts, including permanent damage to the brain and nervous system, leading to decreased IQ.
Economic benefits of eliminating lead exposure:
  Eliminating lead in paint reduces costs to individuals and society that result from exposure to lead (e.g. healthcare, impaired cognitive development, and resulting productivity losses).
  The largest financial burden of lead exposure is borne by low and middle income countries.
  The cost of removing existing lead paint can be substantial. It therefore makes economic sense to enact laws now to prevent future removal costs.
Notes: Background (Excerpted from Guidance):
Exposure Pathways and Health Effects:
The weathering, peeling or chipping of old lead paint releases lead into dust and soil in and around homes, schools and other locations. Lead-containing dust can also be brought into the home on the clothes of those who work in industries where such dust is generated, including paint factories where lead continues to be used.
Lead-contaminated soil and dust are easily inhaled, ingested and absorbed, particularly by young children when they play on the floor or outdoors and put their hands or other objects in their mouths. Children also ingest lead if they mouth and chew toys painted with lead paint. Both children and adults can be exposed to lead in paint chips and dust generated during the removal of old lead paint.
The negative health effects from exposure to lead have been known for many years, and include effects on multiple body systems. Lead can cause permanent damage to the brain and nervous system, resulting in decreased IQ and behavioural problems. It can also cause anaemia, increase the risk of kidney damage and hypertension, and impair reproductive function.
Young children are especially vulnerable to the adverse effects of lead. Even relatively low levels of exposure can cause serious and, in some cases, irreversible neurological damage. There is no known level of lead exposure that is considered safe.
Economics of Lead Exposure:
The negative impacts on children’s developing brains resulting from exposure to lead has staggering economic costs that are borne by the affected children, their families and societies at large. These include health care costs, productivity losses and intellectual disability.
The Institute for Health Metrics and Evaluation has estimated that, based on 2015 data, lead exposures from all sources accounts for 12.4% of cases of idiopathic intellectual disability (i.e., intellectual disability without another known cause).
The largest economic burden of lead exposure is borne by low and middle income countries. Estimated annual costs (in international dollars) of lead exposure by global region, based on loss of IQ, include the following: Africa - $134.7 billion; Latin America and Caribbean - $142.3 billion; and Asia - $699.9 billion.
In addition, the cost of removing existing lead paint from surfaces in homes, schools and other buildings can be substantial. It makes economic sense for countries to enact laws that prevent future removal costs by establishing a legal limit on lead content that will result in lead paint no longer being used in such buildings.

## Slide 10: The Case for Legal Limits
Availability of alternatives:
  The cost of eliminating the use of lead compounds in many paints is low, and many manufacturers have already successfully reformulated paint products to avoid intentionally adding lead.
Proven effectiveness of legal regimes for controlling lead in paint:
  Eliminating the source of lead exposure is the single most effective way of protecting people from the harmful effects of lead.
  Laws have proven effective in controlling use of lead paint in many countries, resulting in reductions in lead poisoning.
  For the paint industry, producing or using paints without added lead compounds can ensure continued access to markets where lead content in paint is already restricted (one third of countries, and counting).
Notes: Background:
The economic cost of eliminating the use of lead compounds in many paints is known to be low, with many manufacturers already successfully reformulating paint products that avoid the intentional addition of lead. According to a paint industry spokesman, “the reformulation of residential and decorative paints to eliminate lead additives is feasible, and the technical and cost impacts are manageable.” [Industry comment from Akzo Nobel] However, the substitution of non-leaded for leaded additives is not one to one. It sometimes requires some research and development on the part of the company and this can be a perceived barrier. There is a need to raise awareness of the companies, in particular small and medium sized enterprises of how to successfully do a substitution. Often pigment and additive vendors will work with clients to accomplish this.
The elimination of lead exposure at its source is the single most effective action to protect people from the harmful effects of lead. The removal of lead from gasoline has produced dramatic reductions in airborne emissions and associated exposures and public health impacts around the globe. Similarly, most industrialized countries adopted laws or regulations to control the lead content of residential and decorative paints in the 1970s and 1980s, based on clear findings that lead-containing paint is a major source of lead exposure in children. The continued use of lead in paint in many parts of the world, however, remains an unaddressed environmental source of human exposure. Laws, regulations or enforceable standards are needed in every country to stop the manufacture, sale and import of lead-containing paints.
Lead paint testing is showing that countries with lead paint laws have lower levels of lead in paint – see South America (IPEN map - http://ipen.org/projects/eliminating-lead-paint/lead-levels-paint-around-world)
Establishing lead paint laws will help countries ensure that not only domestic production but also imported paint and similar surface-coating materials will not include lead above the national legal limit.

## Slide 11: Part 2: Key Provisions of the Model Law for Regulating Lead Paint

## Slide 12: Overview of Key Provisions:
  Legal Limit on Lead Content
  Effective Dates
  Mechanisms to Promote Compliance and Enforcement
  Consequences for Non-Compliance
Notes: Notes: The next set of slides detail key provisions of the Model Law. Each of these provisions is discussed in detail in the Guidance, and the corresponding legal text is contained in the Model Law.

## Slide 13: Establishing a Legal Limit on Lead Content
Why 90 parts per million (ppm)?
  Growing international consensus: 90 ppm is feasible for current detection methods and achievable by manufacturers around the world
Examples of countries with low legal limits:
Kenya (2017)
Paraguay (2017)
Tanzania (2017)
India (2016)
Thailand (2016)
Nepal (2014)
Mexico (2013)
The Philippines (2013)
Jordan (2012)
Argentina (2011)
Sri Lanka (2011)
Uruguay (2011)
South Africa (2009)
Brazil (2008)
Oman (2008)
United States (2008)
Canada (2005)
Switzerland (2005)
Guyana (2004)
Dominica (2002)
Chile (1997)
Panama (1996)
Costa Rica (1994)
Notes: Background (Excerpted from Guidance):
The lowest and most protective maximum regulatory limit that has been set in countries for lead in residential and decorative paints is 90 parts per million (ppm) total lead content, based on the weight of the total non-volatile content of the paint or the weight of the dried paint film. (This specific limit can also be measured and expressed in a law or standard as 0.009 % or 90 mg/kg of total lead, based on the dry weight of the paint film.)
The 90 ppm limit is technically feasible for manufacturers to achieve by avoiding the addition of lead compounds and taking into account residual (unintentional) lead content in certain paint ingredients.
Thus, the model law uses 90 ppm as the total lead limit because it is the lowest limit reflected in existing laws and thus provides the best available health protection, and is technically feasible.
Paint testing conducted by environmental groups in numerous developing countries shows that while high levels of lead are often found, in those same countries levels below 90 ppm are also achievable.
Countries that have set a legal limit of 90 ppm total lead content are: Canada, Paraguay, India, Kenya, Nepal, the Philippines, Tanzania and the United States of America.
Switzerland and Thailand have limits of 100 ppm total lead, while some other countries have adopted a limit of 600 ppm total lead content: Argentina, Brazil, Chile, Costa Rica, Dominica, Guyana, Jordan, Mexico, Oman, Panama, South Africa, Sri Lanka and Uruguay.,
Additional Background:
As the dates on the slides indicate, the trend in recent years among countries enacting lead paint laws is to use 90 ppm
Most new regulations are 90 ppm.
Regulatory levels:
  90 ppm: Kenya (2017), Paraguay (2017), Tanzania (2017), India (2016), Nepal (2014), the Philippines (2013), United States (2008), Canada (2005)
  100 ppm: Thailand (2016), Switzerland (2005)
  600 ppm: Mexico (2013), Jordan (2012), Argentina (2011), Uruguay (2011), Sri Lanka (2011), South Africa (2009), Brazil (2008), Oman (2008), Guyana (2004), Dominica (2002), Chile (1997), Panama (1996), Costa Rica (1994)

## Slide 14: Establishing a Legal Limit on Lead Content
The Model Law lead limit is defined as 90 ppm TOTAL lead
Defining the lead limit in terms of total lead is most protective, as it covers all forms of lead (i.e., soluble lead and insoluble lead, both of which are sources of exposure)
The measurement technique for total lead is more reliable and affordable, and accordingly makes enforcement more effective
Notes: Background (Excerpted from Guidance):
It is important to specify that the legal limit should be defined as 90 ppm “total lead” content rather than “soluble lead” content in paint. The majority of countries with legal limits on lead paint use total lead.
The soluble lead limit approach is the scientifically unsupported premise that exposure comes only from children mouthing or swallowing lead paint or painted objects, and thus does not account for potential exposure from inhalation or ingestion of lead dust. Recent research suggests that particulate (insoluble) lead found in dust, soil and paint chips is a more significant contributor to chronic and acute exposure than soluble lead (such as lead exposure through chewing on a toy).
Further, degrading painted surfaces, as well as weathering and aging, generate paint chips and dust that contaminate house dust and outdoor soils, thus increasing the potential for exposures to insoluble lead.
Finally, it is important to note that all lead in paint, whether soluble or insoluble in a lab test, has the potential to be available for exposure through inhalation or ingestion, especially by young children who crawl and play on the floor and outside on soil.
While there is no safe level of lead exposure, a regulatory limit based on total lead will be more protective of health than a limit based only on soluble lead.

## Slide 15: Establishing a Legal Limit: Scope of Coverage
The Model Law recommends including all paints simplifies enforcement and is most protective
In the event of exceptions for special uses, precautionary labeling should always be used:
  “DANGER: CONTAINS LEAD. DO NOT APPLY TO SURFACES ACCESSIBLE TO CHILDREN OR PREGNANT WOMEN.”
The model law does not recommend labeling provisions for paints as “lead free,” since it is not technically possible to eliminate lead contamination from all ingredients. Instead, setting a very low limit is recommended.
Notes: Background (Excerpted from Guidance):
The Model Law applies the total lead limit to all paints (e.g., household, industrial, agricultural, etc.). It is possible to restrict the use of lead in all paints, and some countries have done so. This has the benefit of protecting the whole population from lead exposure from paint, especially in countries where both household paint and industrial paint are frequently sold side by side in retail markets.
If a country chooses to exempt certain paints from the total lead limit, it should require such paints to bear a legible, visible warning label so that consumers are aware of the health hazards involved with using such exempted paint.
Sample language for a labeling requirement is contained in the Guidance, as well as sample language for the label which is presented on the slide.
Warning labels are strongly advised on any paints exempted from the 90 ppm total lead limit so that consumers receive fair warning about the hazards of using such paints. In contrast, warning labels are not necessary on paints subject to the lead paint law because lead in these paints will be limited to 90 ppm total lead or less and therefore will not present a hazard to consumers.
Additional Background:
Some categories of paints that countries have exempted from the law include artists’ paints and automobile paints. Although un-leaded substitutes are available to make artists’ and automobile paints, the rationale for exempting these paints is that the risk of exposure for children is relatively low, as both types of paint would in theory be inaccessible to children. In practice, however, that may not always be the case, and these paints still pose a risk to workers. For this reason, the model law does not include exceptions.

## Slide 16: Setting Effective Dates
Provides industry with a timeline for compliance
Can choose to use either delayed effective dates for all paints, or phased effective dates for different types of paints (for example, one year for household paints, two years for industrial paints)
Most countries have effective dates of one year or less
Notes: Background (Excerpted from Guidance):
Lead paint laws should specify dates when the requirements set out in the law will come into effect.
In establishing such dates, countries may wish to work with industry to determine a reasonable amount of time needed to source and procure alternative materials, to alter product formulations and processes, and to sell or dispose of existing stocks of paint containing lead above the total lead limit.
One way to allow time for industry to change its practices and come into compliance with the total lead limit is to provide a reasonably delayed effective date for the 90 ppm total lead limit, applicable to all paints covered by the law. Most lead paint laws that limit lead to 90 ppm or 100 ppm have required compliance within one year of passage of the law. Countries limiting lead in paint to 90 ppm that required compliance immediately or within one year include: Canada, India, Kenya, Nepal, Tanzania and the United States. Thailand limits lead to 100 ppm and required compliance within one year. Switzerland limits lead to 100 ppm and required compliance within 15 months.
As an alternative to a broadly applicable delayed effective date for the 90 ppm limit, countries may wish to provide phased effective dates, depending on the type of paint. This approach is designed to take into account the different uses and performance requirements of paints and the relative harms posed by such uses. For example, a law could allow somewhat more time for industrial paints to come into compliance with the total lead limit but less time for decorative paints intended for household use or other applications most likely to contribute to childhood lead exposure. The Philippines is unique in allowing three years for compliance for architectural, decorative and household applications, and six years for industrial applications.

## Slide 17: Compliance and Enforcement Mechanisms
Model law uses a “Declaration of Conformity” process to promote compliance and provide a mechanism for enforcement
A Declaration of Conformity (DoC) is a simplified type of conformity assessment procedure (as opposed to full-scale certification process)
Notes: Background (Excerpted from Model Law):
A declaration of conformity is one type of “conformity assessment” procedure, which is an internationally used term that covers activities used to provide confidence in a product supplier’s compliance with safety, health, environmental and fair commerce requirements.
Conformity assessment systems come in many types, which have varying degrees of complexity and resource investment.
“Certification” is a different type of conformity assessment mechanism that was considered for inclusion in this model law. As this term is used internationally, certification generally has two essential characteristics: (1) it is conducted by a third party and (2) it includes some form of surveillance activity by the third party to ensure ongoing compliance once initial compliance with a requirement has been determined. Many third-party certification bodies use an on-product mark or symbol to attest to the conformity of certified products.
Similar to a certification approach, the declaration of conformity approach used in the model law requires testing by an independent, third-party laboratory accredited under rigorous, internationally-approved standards. Unlike a certification approach, however, the model law does not rely on the creation and involvement of a separate certifying body to ensure ongoing compliance with the lead limit. [KEY POINT if questions are raised about DoC v. certification].
The declaration of conformity approach is recommended and used in the model law because it places the obligation for compliance on manufacturers and importers. It is manufacturers and importers who must ensure testing by an accredited laboratory and must sign a sworn affidavit stating that their paints comply with the 90 ppm total lead limit. Failure to do so subjects these parties to civil, and possibly criminal, penalties.

## Slide 18
Compliance and Enforcement Mechanisms
Third-party laboratory tests paint samples and provides results and attestation to manufacturer / importer.
Paint manufacturer or importer sends samples to accredited third-party laboratory.
Designated agency can request DoC from any person manufacturing, selling, or importing paint. Agency can also inspect facilities where paint is manufactured or held as well as test paint to assess compliance.
Manufacturer or importer creates Declaration of Conformity (DoC) affirming that paint complies with lead limit and provides DoC to distributors and retailers.
1) Manufacturing, selling, or importing paint violating lead limit
AND 2) failure to provide DoC or exercise due care in reviewing legitimacy of DoC are BOTH prohibited.
Notes: Note that importer can rely on foreign manufacturer’s test results to issue a DoC but must exercise due care to ensure test results meet requirements
The Model Law also provides for any person (or entity) to sue to enforce the law, for example to require production of a DoC.

## Slide 19: Compliance and Enforcement Mechanisms
Steps for Importers and Manufacturers:
  Step 1: Submit paint samples for third-party testing
  Step 2: Prepare DoC based on test results
  Step 3: Submit DoC to paint distributors and retailers, and the relevant government agency upon request
  Step 4: Keep records of DoC and related test results for five years
Notes: Background:
This slide lays out the steps that paint manufacturers and importers will need to take in order to comply with the Model Law. The following slides will detail each of these steps.
An important related point here is that, in addition to these mechanisms built into the law itself, governments can also promote compliance by educating industry about the requirements of the law and how to meet the requirements.

## Slide 20: Compliance and Enforcement Mechanisms
Third-Party Testing Requirements
  Who? Manufacturers and importers of paint must ensure testing by third party laboratory
  What? Must submit “sufficient samples” of first production batch of paint, or whenever there is a “material change”
  Where? Samples must go to a third party laboratory accredited under international standards for testing lead paint
Notes: Background (Excerpted from Model Law):
The Model Law requires manufacturers and importers to submit “sufficient samples” of paint or similar surface-coating materials to a third-party laboratory accredited under international standards for testing for compliance with the 90 ppm total lead limit.
“Sufficient samples” is defined as the number of samples the Agency in charge of implementing the lead paint law determines necessary to provide a high degree of assurance that the tests conducted accurately demonstrate the paint or similar surface-coating materials’ compliance with the 90 ppm total lead limit.
  Note that the reason the Model Law uses the term “sufficient samples” instead of a set number is reflective of the different types of surface coatings and production processes, and that there may be variations in the degree of uniformity of different products.
Testing the first production batch or lot will be sufficient to meet the testing requirement unless a material change occurs in the production process for that paint product, such as a change in ingredients or a change in an ingredient supplier.
A “material change” is defined as follows: “Material Change” means a change that the manufacturer or importer makes to the design, manufacturing process, or the source of component parts, for the paint or similar surface-coating material, which a manufacturer or importer, exercising due care, knows, or should know, could affect compliance with the 90 ppm total lead limit”
In the event of a material change in the production process, the law should require new third-party testing to be conducted and new declarations of conformity to be issued.
Additional Background:
Testing different shades of paint: In order to comply with the Model Law, a paint company would use third-party testing for a base paint color and any tints as a way to prove that a specific paint shade that results from combining the base with a tint is in compliance with the legal limit. The company would need to provide a declaration of conformity for each paint shade, but could simply specify which ingredients were used in the final paint product plus the test results for each of those ingredients, rather than having to actually test the final paint product.

## Slide 21: Compliance and Enforcement Mechanisms
Third-Party Testing Requirements (continued)
  Meaning of “third party laboratory”:
    Independent: no financial interest in test results
    Accredited: accredited under international standards by an internationally recognized body
  Model Law Appendix 2 lists acceptable international standards for sample preparation and test methods
    International Standards Organization (ISO)
    American Society for Testing & Materials (ASTM) International
Notes: Background (Excerpted from Model Law):
The Model Law defines a third party laboratory as follows:
  “Third-party laboratory” means an independent laboratory that has no interest in the transaction between the manufacturer or importer and the distributor or retailer, and that has been accredited under ISO/IEC 17025 by a signatory to the International Laboratory Accreditation Cooperation (ILAC) Mutual Recognition Arrangement (MRA), or one of its recognized regional bodies: Inter American Accreditation Cooperation (IAAC), European co-operation for Accreditation (EA), Asia Pacific Laboratory Accreditation Cooperation Incorporated (APLAC).”
The Model Law further provides that, for a third-party laboratory’s “accreditation to be accepted to test for the 90 ppm total lead limit for declaration of conformity purposes, a third-party laboratory shall be accredited for and use” certain internationally recognized sampling and test methods. The Model Law does not choose among those methods, but rather provides countries with a list of currently accepted methods and standards, and also recommends including language recognizing and accounting for changes in test methods over time as science advances.

## Slide 22: Compliance and Enforcement Mechanisms
Third-Party Testing Requirements (continued)
  In-country lab capacity should not be a barrier to implementation or compliance
    If country is only importing paint, lab capacity not necessarily needed in each country – importers can use lab data from exporting country (see next slide)
    If exporting, lab capacity can be met by the international lab community through the International Laboratory Accreditation process
Notes: Background (excerpted from Guidance):
Countries should encourage laboratories to acquire the necessary equipment, expertise, and accreditation to perform the required testing of lead paint.
That said, current lack of in-country laboratory capacity need not be an impediment to a lead paint law going into effect, as industry can still comply with the law by sending paint samples to laboratories in other countries that are qualified to perform the required testing.
Additionally, for imported paints, manufacturers and importers can rely on test results from qualified laboratories in the country of origin under the model law under certain circumstances (see next slide).

## Slide 23: Compliance and Enforcement Mechanisms
Importers: Reliance on Foreign Third-Party Testing Results
  Model law provides that an importer can sometimes rely on a foreign paint manufacturer’s test results to issue its own declaration of conformity (see below)
  Importer must exercise due care to ensure the foreign test results meet the third-party testing requirements of the law, including keeping records of the test results, and reviewing how the testing was conducted
Notes: Background (Excerpted from Guidance):
In order to ensure that testing is not unduly burdensome and duplicative, importers may be allowed to rely on a foreign manufacturer’s test results to issue the importer’s declaration of conformity, as long as the importer exercises due care to ensure that the manufacturer’s test results meet the requirements of the law, and the importer maintains appropriate records of the test methodology and results.
Additional Background:
The concept of “due care” is found in the legal frameworks of many countries, and refers here to the importer’s responsibility to ensure that the foreign manufacturer’s testing, upon which the importer intends to rely to issue its declaration of conformity, meets the requirements of the law. If that term is not one found in a particular country’s lexicon, an analogous term could be used.
It’s critical for the importer to exercise due care to ensure that the manufacturer’s testing was done according to the law, by an accredited third party lab, using the appropriate test methods rather than simply relying on the manufacturer’s testing to safeguard against a scenario where the importer is dealing with paint above the legal limit.
If an importer fails to exercise due care, and it turns out that the foreign manufacturer falsified test results or didn’t use an accredited lab, etc., and the importer relies on the false testing to issue a declaration of conformity, and it ends up that the paint doesn’t meet the 90 ppm, then the importer would be liable for issuing a false declaration.
The importer would not be liable for issuing a false declaration if she/he exercised due care and did not have reason to know the declaration was false or misleading (e.g., if there was fraud by the foreign manufacturer or the lab).

## Slide 24: Compliance and Enforcement Mechanisms
Content of Declaration of Conformity
  Sworn affidavit signed by manufacturer or importer
  Identification of the paint covered
  Name/contact for manufacturer or importer
  Contact information for laboratory and individual maintaining records of test results
Manufacturers and importers must provide the completed DoC to paint distributors and retailers
Notes: Background:
As indicated previously, one of the beneficial features of a Declaration of Conformity process is that it puts the obligation to ensure that paint is meeting the legal limit on the manufacturers and importers, who also must bear the consequences if the paint is found to be out of compliance.
A key feature of the Declaration of Conformity is a sworn affidavit/attestation by the manufacturer or importer asserting that they have arranged for the required third party testing, and based on those results, their product complies
Another key piece of information is the contact information for the laboratory and individuals maintaining the test results, and the government may use that information in conducting inspections.
The Model Law requires that paint manufacturers and importers give copies of the completed DoC to paint distributors and retailers, which provides those entities with assurance that the paint they are selling complies with the law. Provide could mean to physically provide, or to give access to the DoC via a website, such as if a manufacturer or importer opts to create a website where distributors and retailers can view and download the DoC.

## Slide 25: Compliance and Enforcement Mechanisms
Government Role in Ensuring Compliance
  Government Inspections
    Enter facility or store to inspect and to view testing data/Declaration of conformity and related records
    Ensures law is being followed
  Government Testing
    Governments have authority to test paint
Notes: Background (Excerpted from Guidance):
Inspections by the government agency in charge of implementing the lead paint law are critical to ensuring that paints are manufactured and imported in conformity with the country’s total lead limit.
The Model Law authorizes government agents to enter a location at reasonable times to inspect and test paint or similar surface-coating materials as long as the agents first present appropriate credentials to the owners, operators or agents of the location.
The Model Law also authorizes the government to test paints in a reasonable manner in order to assess compliance with the law.
Additional Background:
The model law does not require that governments use third-party testing, and testing to confirm compliance can be done in government labs. However, as discussed earlier, there are numerous benefits to using accredited labs due to reliability and accuracy of test results. [Note this last point may be politically sensitive, depending on the audience]. In enforcement actions, there may be a benefit to using a third party lab to conduct testing, as then there can be no basis for allegations by the regulated entities of any impropriety in the testing.

## Slide 26: Compliance and Enforcement Mechanisms
What actions constitute a violation of the law?
  Manufacturing, selling, distributing, or importing paint containing lead over the legal limit
    KEY: Because sale and distribution of lead paint is prohibited, retailers and distributors are incentivized to check the declarations of conformity they receive from manufacturers, or importers.
  Failing to cooperate with government inspectors/testing
  Failing to provide a DoC or making a false declaration
  Attempting to exert undue influence over third party laboratory testing the paint
Notes: Background:
This slide describes the actions the Model Law defines as “prohibited acts”
Additional Background (relates to next slide as well):
The model law makes it a prohibited act to sell or distribute paint with lead levels above the legal limit. This would mean that it would be a prohibited act for a paint retailer to sell paint that it received from a manufacturer with a seemingly valid Declaration of Conformity, even if the manufacturer had forged the Declaration and the paint actually had higher levels of lead. That instance, however, highlights that the government has discretion in assigning penalties for the various prohibited acts. There, the government would seize all the effected paint, and the paint retailer could get a nominal monetary fine, while the manufacturer that forged the Declaration could get extensive fines and possible additional penalties.

## Slide 27: Enforcement and Consequences for Non-Compliance
What are the penalties for failing to follow the law?
  Civil monetary penalties
  Criminal penalties
  Other appropriate relief or sanctions
Citizen Suits: an additional means to enforce the law and promote compliance
Notes: Background (Excerpted from Guidance):
The Guidance explains how countries can implement these provisions, depending on the country’s current criminal and civil code:
  Where a country already has general legal provisions relating to civil penalties and criminal sanctions for offences, it may wish to refer to those provisions of its parent legislation in its lead paint law.
  If a country does not already have parent legislation relating to penalties or sanctions, or wishes to incorporate independent, specific civil and criminal penalty provisions within its lead paint law, the model law provides sample language.
In addition to specifying meaningful penalties for non-compliance, effective lead paint laws identify remedies such as injunctive relief and seizure or recall of paints that do not comply with the total lead limit.
The Model Law also includes provisions to enable citizens and other “persons” to bring actions to enforce the law. The Model Law defines “person” to include an individual, partnership, corporation, association, or non-profit. Enforcement by citizens and non-government organizations can help to ensure compliance, and assist the government who may have limited capacity to conduct enforcement activities. Paint companies can also use this provision to ensure their competitors are complying with the law.

## Slide 28: Part 3: Key Considerations for Adapting the Model Law to Fit National Conditions and Needs

## Slide 29: Model Law: Key Considerations
Model law can be used to draft a statute, regulation, or standard
  Different countries have taken different approaches, depending on their individual legal frameworks
Potential benefits from using a public process to adopt a lead paint law include:
  Buy-in from key stakeholder groups
  Valuable technical input from industry
Model law and guidance is intended to be a “living document,” i.e., the Lead Paint Alliance will continue to collect feedback and provide clarity where needed

## Slide 30: Thank you!