## Slide 1: Mercury Cell Conversion or Decommissioning: Clean-up and disposal issues
Peter Maxson, Director
Concorde East/West Sprl
UNEP Global Mercury Chlor-alkali Partnership
Expert Group Meeting to Identify Barriers and Opportunities
Vienna, Austria
28-29 June 2016

## Slide 2: Overview
Conversion issues
Planning for conversion or decommissioning
Evaluating facilities for conversion vs decommissioning
Implementing conversion activities
Site clean-up
Mercury storage and disposal

## Slide 3
Chlor-alkali plant (now closed) at Skoghall, Sweden

## Slide 4
One-half of 300,000-tonnes/year mercury chlorine electrolysis plant in Germany. The cells run horizontally across the view of this cellroom. Each cell is 14 metres in length and 2.2 metres wide.
(Euro Chlor)

## Slide 5: Planning for conversion or decommissioning
Clean-up needs to be part of the planning process
  standards
  scope = soil surface area, depth
  old disposal sites
  who and how many contractors
  sequence of process shut-down and clean-up tasks
  reporting
  plan for surprises = contingencies
  estimated cost
  sources of financial assistance

## Slide 6
- - - - - Main changes when converting mercury cell to membrane

## Slide 7: Pioneer Americas LLC - St. Gabriel Plant
Commissioned in 1970 in St. Gabriel, Louisiana.
52 x 30m2 UHDE Mercury Cells

## Slide 8: Cellroom emission improvements
From 1997 to 2003 the Pioneer St. Gabriel Plant has invested over $12,000,000 in 26 improvement projects!

## Slide 16: Decommissioning vs. conversion
Realities of clean-up may influence the initial preference for conversion; in addition to process, space, time, etc. considerations:
  mercury brine system can be reused after careful cleaning, but replace piping to avoid brine recontamination
  reuse of existing process piping is not appropriate
  cell room building structure may be in poor condition
  mercury contamination of existing concrete structures is common

## Slide 17: Decommissioning
planning
setting up a working area
emptying the cells and collecting the mercury
dismantling, demolition and decontamination of equipment and buildings
residual wastes may be stored (briefly) on site, transported and/or further treated before disposal

## Slide 18: Planning
procedures and instructions for all stages of implementation, including health and safety
detailed training and supervision programme for personnel with no experience in mercury handling
suitable working area
equipment for mercury handling (e.g. containers, cranes, forklift trucks, devices to fill containers)
determination of the quantity of metallic mercury to be recovered
estimation of the quantity of waste to be disposed of and of the mercury content
monitoring of mercury in air, water and waste, including after completion
health checks and biological mercury monitoring for staff
planning of transport, storage and disposal

## Slide 19: Working area
well-defined, if necessary surrounded by curbs;
covered to exclude rainwater
equipped with a smooth, sloped, impervious floor to direct mercury spills to a collection sump
well-lit to enable easy identification and clean-up of spills
free of obstructions and debris that may absorb mercury and/or hinder the clean-up of spills (e.g. wooden pallets)
water supply for washing
aspiration equipment with activated carbon filters to rapidly clean up spills
waste water treatment system.

## Slide 20: Emptying the cells
special containers
keeping the system closed, if possible
washing of mercury to remove residual sodium to avoid the risk of hydrogen formation
using gravity transfer, if possible
checking that the mercury is not contaminated and, when necessary, using filtration or decantation to remove solid impurities
avoiding the introduction of other liquids, such as water
filling the containers to ≤ 80 % of their volumetric capacity to avoid overpressures
hermetically sealing the containers after filling
weighing and labelling the containers according to legislation
washing of the empty cells with an alkaline hydrogen peroxide solution and water, then filling with water to reduce mercury emissions until the cells are dismantled.

## Slide 21: Dismantling, demolition and decontamination
inclusion of staff experienced in running the former plant
replacement of hot cutting of equipment by cold cutting, if possible
taking precautions against the dispersion of mercury droplets if high pressure is used for cleaning of surfaces
storage of contaminated equipment in suitable areas (e.g. steel may be highly contaminated with mercury which can sweat out during storage)
frequent washing of the floor of the working area
rapid clean-up of mercury spills by using aspiration equipment with activated carbon filters
accounting of waste streams (origin, mass, volume, mercury concentration and destination)

## Slide 22: Treatment techniques for solid waste
Mechanical and physical treatments = washing with water (with or without pressure), ultrasonic vibration, and vacuum cleaners with appropriate adsorption or condensation systems. Mechanical and physical treatments are suitable if significant quantities of metallic mercury are present.
Chemical treatment = treatment with hypochlorite, chlorinated brine or hydrogen peroxide. The liquid streams are treated as described below.
Thermal treatment = distillation/retorting carried out in specially designed units. Mercury recovered as metallic mercury.

## Slide 23
Spanish mercury-cell chlor-alkali plant. The red painted installation (centre) shows the new unit to recover mercury from the hydrogen stream. To achieve better environmental control, 40% of the existing plant was moved and upgraded from the brown building in the background to a new green building on the right. 60% of the plant remained unchanged in a building located just out of the picture. (Euro Chlor)

## Slide 24
FOOTBALL FIELD-SIZED --A typical mercury-cell chlor-alkali plant's cell room holds 50 to 100 mercury cells, more than a mile of pipes, hundreds of pumps and flanges....
PIONEER AMERICAS