## Slide 1: Chlor Alkali Industry Indian Experience
Satish Sinha
Toxics Link

## Slide 2: Global capacity- chlor alkali
Chart: 
| Global | India
Production | 102 | 3.4
Chart: India- Technology
| Cell Membrane | Mercury
Technology | 100 | 0
Cell membrane technology- first commercial plant commissioned in 1975 in Japan
Chemfab Alkalis -first ones to shift to membrane technology in India in 1985.

## Slide 3: Industry overview
First Plant 1959
First conversion to Membrane 1985
Total number of plants 32
Number of plants closed 5
Installed capacity 3.39 MMTA
Production 2.76 MMTA
Capacity utilization 81%

## Slide 4: Factors influencing technology shift
Reduction in energy consumption
Expansion in plant capacity
Addressing environmental concerns
Availability of technology UDHE, De Nora and Ashai
Regulatory compliance benefits
Indirect benefits to community , workers relations and health

## Slide 5: Charter on Corporate responsibility for Environmental Protection- 2003 ( CREP)
17 industrial sectors
Shift to Membrane technology by 2012
Mercury distillation
De-mercurisation of caustic soda
Reduction of mercury consumption
Reduced mercury release

## Slide 6: Economic outlook Chemical industry
Indian GDP- Between 7 & 8%
Chemical market – growth between 2009-14 around 14-15%- Future projection 10-13%
Chlor Alkali growth rate 5 % against 7-8%
Anti dumping duty and strengthening of caustic soda prices around 2009
Chemical growth statistics- FICCI
http://forum.valuepickr.com/t/chemfab-alkalis-well-poised-for-the-caustic-soda-chlorine-cycle/1202/2
Notes: 12
th
In
12th largest producer of chemicals globally

## Slide 7
Anti dumping duty on imports - strengthening of domestic prices

## Slide 8: Economic Driver
Energy requirement 60-70%
Mercury cell 3000 kwh/t
Membrane cell 2300-2400 kwh/t
Net saving > 20%
Saving per/ton 3670 INR

## Slide 9: Cost consideration
Cost of conversion 100 ton plant 11-12 m USD
Cost of conversion Indian Industry 750 m USD
Import duty reduction 4%
Membrane replacement 3-5 years
Indigenous manufacturing
Maintenance cost 3% /project cost
Return on investment without 7 years
expansion
With 20% expansion 5 Years

## Slide 10
Membrane cell advantages
Improved product quality
Mercury free - toxicity reduction
Energy savings - Reduced carbon footprint and costs
Reduction in mercury management costs

## Slide 11: Protocol Mercury Management
Increase in capacity or new site- EIA
Mercury management plan for partial or complete conversion
Reuse of excess mercury, status unknown ?
Removal of mercury from pipelines, equipments
Testing of ground water and soil , remedial action
Not viable for old plants - leading to closure

## Slide 12: Lessons learnt
Environment consideration key driver
Critical business decision
Analyze business information from each country
Age of existing plants and its viability for shifting
Capital intensive