## Slide 1
Shunichi Honda PhD
Section Chief
Ministry of the Environment, JAPAN
shunichi_honda@env.go.jp
Ministry of the Environment
Government of Japan
Japan’s Experience in Mercury Management
Execom Meeting,
Surabaya
29-30 July 2011

## Slide 2
1 | Government Measures
2 | Measures of Industrial Processes
3 | Mercury Waste Management
Contents
Hg Execom, 29-30 Jul 2011, Honda

## Slide 3
1. Government Measures
Hg Execom, 29-30 Jul 2011, Honda

## Slide 4
1. Government Measures
- Control of Hg Use in Products -
Cosmetics | Ban of the use of Hg and its compound
Agricultural chemicals | Ban of the sales and use of agricultural chemicals containing Hg and its compound
Sludge fertilizer | Not exceeding 0.005 mg-THg/L, not detecting Alkyl-Hg
Product recycled from sludge | Not exceeding 0.0005mg-THg/L, not detecting Alkyl-Hg
Household commodity | Not detecting organic mercury compounds
Pharmaceutical products | Not allowed of Hg compound (exemption: if no alternatives exist)
Hg Execom, 29-30 Jul 2011, Honda

## Slide 5
2. Measures of Industrial Processes
- Hg Demand Reduction in Products and Industries -
About 12 tons/year
Hg Execom, 29-30 Jul 2011, Honda

## Slide 6
2. Measures of Industrial Processes
- Hg Demand Reduction in Caustic Soda Production -
Hg Execom, 29-30 Jul 2011, Honda
1973 | 113.9 g-Hg/ 1 t-caustic soda production
1979 | 2.3 g-Hg/ 1 t-caustic soda production
1986 | Phase-out of Hg process
Ion-exchange membrane
Diaphragm
Mercury
1999 | Phase-out of Diaphragm

## Slide 7
2. Measures of Industrial Processes
- Hg Demand Reduction in Batteries -
About 1 ton/year
1970- | Hg emission emitted from incinerators which incinerated MSW with Hg cells
1983 | Governmental instruction to reduce Hg content in cells and take-back waste cells
1991 | Hg free manganese cells
1992 | Hg free alkaline cells
1995 | End of Hg cell production
Hg Execom, 29-30 Jul 2011, Honda

## Slide 8
2. Measures of Industrial Processes
- Hg Demand Reduction in Lamps -
mg/unit
Average Hg Content in FL
Hg Use in Hg-Lamps
Policy for Procurement (2001-) | 
FL (40W straight) | 10 mg or less
Bulb-type FL | 5 mg or less
2002 | Updated manual to reduce Hg content in lamps
2005 | Guidelines for Hg content in lamps
Hg Execom, 29-30 Jul 2011, Honda

## Slide 9
2. Measures of Industrial Processes
- Hg Demand Reduction in Medical Equipment -
Hg-in-glass manometers and thermometers → Digital manometers and thermometers
Hg Execom, 29-30 Jul 2011, Honda

## Slide 10
3. Mercury Waste Management
- Municipal/Industrial Waste Collection System -
Wastes
MSW
Industrial wastes
Other wastes
Night solids
Oversized wastes
Specially controlled MSW
Wastes from households
Wastes from businesses
Specially controlled industrial wastes
Ashes, sludge, waste oil, waste acid, waste alkali, waste plastics and others from businesses
Business's responsibility
Municipality's responsibility
Medical devices, etc
Wastes
contaminated
with Hg
Hg wastes
FL, batteries, thermometers, etc
FL, batteries, thermometers, etc
Other wastes
Wastes
contaminated
with Hg
Hg Execom, 29-30 Jul 2011, Honda

## Slide 11
3. Mercury Waste Management
- Voluntary Collection of Button Cells -
Hg Execom, 29-30 Jul 2011, Honda

## Slide 12
3. Mercury Waste Management
- Hg Waste Treatment -
Hg Execom, 29-30 Jul 2011, Honda

## Slide 13
3. Mercury Waste Management
- Material Flow of Hg (2002-2006 data) -
Hg Execom, 29-30 Jul 2011, Honda

## Slide 14
www.env.go.jp/chemi/tmms/pr-m/mat01/en_full.pdf
Lessons from Minamata Disease
And Mercury Management in Japan
January 2011
Ministry of the Environment, Japan